## Slide 1: SVA Advanced Topics: SVAUnit and Assertions for Formal

## Slide 2: SystemVerilog Assertions Verification with SVAUnit
Andra Radu Ionuț Ciocîrlan

## Slide 3: Tutorial topics
Introduction to SystemVerilog Assertions (SVAs)
Planning SVA development
Implementation
SVA verification using SVAUnit
SVA test patterns

## Slide 4: Introduction to SystemVerilog Assertions (SVAs)

## Slide 5: Assertions and properties
What is an assertion?
What is a property?
assert (a |-> b)
else $error("Assertion failed!")
property p_example;
a |-> b
endproperty

## Slide 6: Simple assertion example
property req_to_rise_p;
@(posedge clk) $rose(req) |-> ##[1:3] $rose(ack);
endproperty
ASSERT_LABEL: assert property (req_to_rise_p)
else `uvm_error(“ERR", "Assertion failed")

## Slide 7: Types of SystemVerilog Assertions
Immediate
Concurrent
assert (expression) pass_statement
[else fail_statement]

## Slide 8: Assertions are used
In a verification component
In a formal proof kit
In RTL generation
  “Revisiting Regular Expressions in SyntHorus2: from PSL SEREs to Hardware” (Fatemeh (Negin) Javaheri, Katell Morin-Allory, Dominique Borrione)
For test patterns generation
  “Towards a Toolchain for Assertion-Driven Test Sequence Generation” (Laurence PIERRE)

## Slide 9: SVAs advantages
Fast
Non-instrusive
Flexible
Coverable

## Slide 10: Planning SVA development

## Slide 11: Identify design characteristics
Defined in a document (design specification)
Known or specified by the designer
The most common format is of the form cause and effect: antecedent |-> consequent
  Antecedent:
  Consequent:
  $rose(req)
  ##[1:3] $rose(ack)

## Slide 12: Keep it simple. Partition!
Complex assertions are typically constructed from complex sequences and properties.
a ##1 b[*1:2] |=> c ##1 d[*1:2] |=> $fell(a)
sequence seq(arg1, arg2);
arg1 ##1 arg2[*1:2];
endsequence
seq(a, b) |=> seq(c, d) |=> $fell(a)

## Slide 13: Implementation

## Slide 14: Coding guidelines
Avoid duplicating design logic in assertions
Avoid infinite assertions
Reset considerations
Mind the sampling clock

## Slide 15: Coding guidelines (contd.)
Always check for unknown condition (‘X’)
Assertion naming
Detailed assertion messages
Assertion encapsulation

## Slide 16: Best practices
Review the SVA with the designer to avoid DS misinterpretation
Use strong in assertions that may never complete:
Properties should not hold under certain conditions (reset, enable switch)
assert property ( req |-> strong(##[1:$] ack));
assert property (
@(posedge clk) disable iff (!setup || !rst_n)
req |-> strong(##[1:$] ack)
);

## Slide 17: Best practices (contd.)
Avoid overlapping assertions that contradict each other
CPU_0:
CPU_1:
assert property (WRITE |=> ERROR);
assert property (WRITE |=> !ERROR);
assert property (WRITE and CPU==0 |=> ERROR);
assert property (WRITE and CPU==1 |=> !ERROR);

## Slide 18: Best practices (contd.)
Use the $sampled() function in action blocks
Active
Inactive
NBA
Observed
Re-active
Re-inactive
Postponed
Preponed
Previous timeslot
Next timeslot
assert property ( @(posedge clk) ack == 0 )
else
`uvm_error("ERROR", $sformatf("Assertion
failed. ack is %d", $sampled(ack)));

## Slide 19: Assertion example
AMBA APB protocol specification:
  The bus only remains in the SETUP state for one clock cycle and always moves to the ACCESS state on the next rising edge of the clock.

## Slide 20: Assertion example (contd.)
Antecedent (the SETUP phase)
Consequent (the ACCESS phase)
sequence setup_phase_s;
$rose(psel) and $rose(pwrite)
and (!penable) and (!pready);
endsequence
sequence access_phase_s;
$rose(penable) and $rose(pready) and
$stable(pwrite) and $stable(pwdata)and $stable(paddr) and $stable(psel);
endsequence

## Slide 21: Assertion example (contd.)
The property can be expressed as:
The assertion will look like:
property access_to_setup_p;
@(posedge clk) disable iff (reset)
setup_phase_s |=> access_phase_s;
endproperty
assert property (access_to_setup_p)
else `uvm_error("ERR", "Assertion failed")

## Slide 22: Does it work as intended?

## Slide 23: SVA Verification with SVAUnit

## Slide 24: SVA Verification Challenges
Clear separation between validation and SVA definition code
Easy to:
Update
Enhance
Disable
Results should be:
- Deterministic
Repeatable
Self-contained
Adaptable
Predictable

## Slide 25: Introducing SVAUnit
  Structured framework for Unit Testing for SVAs
  Allows the user to decouple the SVA definition from its validation code
  UVM compliant package written in SystemVerilog
  Encapsulate each SVA testing scenario inside an unit test
  Easily controlled and supervised using a simple API

## Slide 26: SVAUnit Infrastructure
SVAUnit Testbench
SVAUnit Test Suite
SVAUnit Unit Test
SVAUnit Test
test()
SVA interface handle
Interface containing SVA
Interface containing SVA
SVAUnit Test
SVAUnit Test Suite
Reports
Reports
Reports
Reports
  SVAUnit Testbench
  Enables SVAUnit
  Instantiates SVA interface
  Starts test
  SVAUnit Test
  Contains the SVA scenario
  SVAUnit Test Suite
  Test and test suite container

## Slide 27: Example specification
AMBA APB protocol specification:
  The bus only remains in the SETUP state for one clock cycle and always moves to the ACCESS state on the next rising edge of the clock.

## Slide 28: Example APB interface
interface apb_if (input pclk);
logic psel;
logic pwrite;
logic penable;
logic pready;
logic [`ADDR_WIDTH-1 :0] paddr;
logic [`WDATA_WIDTH-1:0] pwdata;
endinterface
APB sequences definitions
APB property definition
APB assertion definition

## Slide 29: APB sequences definitions
Antecedent (the SETUP phase)
Consequent (the ACCESS phase)
sequence setup_phase_s;
$rose(psel) and $rose(pwrite)
and (!penable) and (!pready);
endsequence
sequence access_phase_s;
$rose(penable) and $rose(pready) and
$stable(pwrite) and $stable(pwdata)and $stable(paddr) and $stable(psel);
endsequence

## Slide 30: APB property & assertion definitions
The property can be expressed as:
The assertion will look like:
property access_to_setup_p;
@(posedge clk) disable iff (reset)
setup_phase_s |=> access_phase_s;
endproperty
assert property (access_to_setup_p)
else `uvm_error("ERR", "Assertion failed")

## Slide 31: Example of SVAUnit Testbench
module top;
// Instantiate the SVAUnit framework
`SVAUNIT_UTILS
...
// APB interface with the SVA we want to test
apb_if an_apb_if(.clk(clock));
initial begin
// Register interface with the uvm_config_db
uvm_config_db#(virtual an_if)::
set(uvm_root::get(), "*", “VIF", an_apb_if);
// Start the scenarios
run_test();
end
...
endmodule

## Slide 32: Example of SVAUnit Test
class ut1 extends svaunit_test;
// The virtual interface used to drive the signals
virtual apb_if apb_vif;
function void build_phase(input uvm_phase phase);
// Retrieve the interface handle from the uvm_config_db
if (!uvm_config_db#(virtual an_if)::get(this, "", “VIF", apb_vif))
`uvm_fatal(“UT1_NO_VIF_ERR", "SVA interface is not set!")
// Test will run by default;
disable_test();
endfunction
task test();
// Initialize signals
// Create scenarios for SVA verification
endtask
endclass

## Slide 33: APB – SVAUnit test steps
Enable the APB SVA
Initialize the interface signals
Generate setup phase stimuli
Generate access phase stimuli
SVA checks based on generated stimuli

## Slide 34: Enable SVA and initialize signals
...
// Enable the APB SVA
vpiw.disable_all_assertions();
vpiw.enable_assertion("APB_PHASES");
// Initialize signals
task initialize_signals();
apb_vif.paddr <= 32'b0;
apb_vif.pwdata <= 32'b0;
apb_vif.pwrite <= 1'b0;
apb_vif.penable <= 1'b0;
apb_vif.psel <= 1'b0;
endtask
...

## Slide 35: Generate setup phase stimuli
...
task generate_setup_phase_stimuli(bit valid);
...
// Stimuli for valid SVA scenario valid == 1 ->
pwrite == 1 && psel == 1 && penable == 0 && pready == 0;
// Stimuli for invalid SVA scenario valid == 0 -> pwrite != 1 || psel != 1 || penable != 0 || pready != 0;
...
endtask
...

## Slide 36: Generate access phase stimuli
...
task generate_access_phase_stimuli(bit valid);
...
// Constrained stimuli for valid SVA scenario valid == 1 ->
pwdata == apb_vif.pwdata && paddr == apb_vif.paddr &&
pwrite == 1 && psel == 1 && penable == 1 && pready == 1;
// Constrained stimuli for invalid SVA scenario valid == 0 ->
pwdata != apb_vif.pwdata || paddr != apb_vif.paddr ||
pwrite != 1 || psel != 1 || penable != 1 || pready != 1;
...
endtask
...

## Slide 37: SVA state checking
...
if (valid_setup_phase)
if (valid_access_phase)
vpiw.fail_if_sva_not_succeeded("APB_PHASES",
"The assertion should have succeeded!");
else
vpiw.fail_if_sva_succeeded("APB_PHASES",
"The assertion should have failed!");
else
vpiw.pass_if_sva_not_started("APB_PHASES",
"The assertion should not have started!");
...

## Slide 38: Example of SVAUnit Test Suite
class uts extends svaunit_test_suite;
// Instantiate the SVAUnit tests
ut1 ut1;
...
ut10 ut10;
function void build_phase(input uvm_phase phase);
// Create the tests using UVM factory
ut1 = ut1::type_id::create("ut1", this);
...
ut10 = ut10::type_id::create("ut10", this);
// Register tests in suite
`add_test(ut1);
...
`add_test(ut10);
endfunction
endclass

## Slide 39: SVAUnit Test API
CONTROL
disable_all_assertions();
CHECK
fail_if_sva_does_not_exists(sva_name, error_msg);
REPORT
print_status();
enable_assertion(sva_name);
enable_all_assertions(); . . .
pass_if_sva_not_succeeded(sva_name, error_msg);
pass/fail_if(expression, error_msg); . . .
print_sva();
print_report(); . . .

## Slide 40: SVAUnit Flow
Instantiate test in Test Suite
Create an SVAUnit Test Suite
Register tests in test suite
Scan report
Simulate
Create SVAUnit Testbench
Create an SVAUnit Test
Implement test() task

## Slide 41: Error reporting
Name of SVAUnit check
Custom error message
Name of SVA under test
SVAUnit test path

## Slide 42: Hierarchy report

## Slide 43: Test scenarios exercised

## Slide 44: SVAs and checks exercised

## Slide 45: SVA test patterns

## Slide 46: Simple implication test
a and b |=> c
repeat (test_loop_count) begin
randomize(stimuli_for_a, stimuli_for_b, stimuli_for_c);
interface.a <= stimuli_for_a;
interface.b <= stimuli_for_b;
@(posedge an_vif.clk);
interface.c <= stimuli_for_c;
@(posedge interface.clk);
@(posedge interface.clk);
if (stimuli_for_a == 1 && stimuli_for_b == 1)
if (stimuli_for_c == 1)
vpiw.fail_if_sva_not_succeeded("IMPLICATION_ASSERT",
"The assertion should have succeeded!");
else
vpiw.fail_if_sva_succeeded("IMPLICATION_ASSERT",
"The assertion should have failed!");
else
vpiw.pass_if_sva_not_started("IMPLICATION_ASSERT",
"The assertion should not have started!");
end

## Slide 47: Multi-thread antecedent/consequent
$rose(a) ##[1:4] b |-> ##[1:3] c
repeat (test_loop_count) begin
// Generate valid delays for asserting b and c signals
randomize(delay_for_b inside {[1:4]}, delay_for_c inside {[1:3]});
interface.a <= 1;
repeat (delay_for_b)
@(posedge interface.clk);
interface.b <= 1;
vpiw.pass_if_sva_started_but_not_finished("MULTITHREAD_ASSERT",
"The assertion should have started but not finished!");
repeat (delay_for_c)
@(posedge interface.clk);
interface.c <= 1;
vpiw.pass_if_sva_succeeded("MULTITHREAD_ASSERT",
"The assertion should have succeeded!");
end

## Slide 48: Multi-thread antecedent/consequent (contd.)
$rose(a) ##[1:4] b |-> ##[1:3] c
repeat (test_loop_count) begin
// Generate invalid delays for asserting b and c signals
randomize(delay_for_b inside {[0:10]}, delay_for_c inside {0,[4:10]});
interface.a <= 1;
repeat (delay_for_b)
@(posedge interface.clk);
interface.b <= 1;
vpiw.pass_if_sva_not_succeeded("MULTITHREAD_ASSERT",
"The assertion should have failed!");
repeat (delay_for_c)
@(posedge interface.clk);
interface.c <= 1;
if (delay_for_b < 5)
vpiw.fail_if_sva_succeeded("MULTITHREAD_ASSERT",
"The assertion should have failed!");
end

## Slide 49: Consecutive repetition
a |-> b[*1:2] ##1 c
repeat (test_loop_count) begin
randomize(stimuli_for_a, stimuli_for_c, number_of_b_cycles <= 2);
interface.a <= stimuli_for_a;
repeat (number_of_b_cycles) begin
randomize(stimuli_for_b)
interface.b <= stimuli_for_b;
if (stimuli_for_b == 1) number_of_b_assertions += 1;
@(posedge interface.clk);
end
if (stimuli_for_a == 1 && number_of_b_assertions == number_of_b_cycles &&
number_of_b_assertions > 0)
vpiw.pass_if_sva_started_but_not_finished("IMPLICATION_ASSERT",
"The assertion should have started but not finished!");
@(posedge interface.clk);
... // (continued on the next slide)

## Slide 50: Consecutive repetition (contd.)
a |-> b[*1:2] ##1 c
...
// (continued from previous slide)
interface.c <= stimuli_for_c;
@(posedge interface.clk);
if (stimuli_for_a == 1)
if (number_of_b_assertions != number_of_b_cycles ||
number_of_b_assertions == 0 ||
stimuli_for_c == 0)
vpiw.fail_if_sva_succeeded("IMPLICATION_ASSERT",
"The assertion should have failed!");
else
vpiw.fail_if_sva_not_succeeded("IMPLICATION_ASSERT",
"The assertion should have succeeded!");
end // end of test repeat loop

## Slide 51: Repetition range with zero
a |-> b[*0:2] ##1 c
repeat (test_loop_count) begin
randomize(stimuli_for_a, stimuli_for_c, number_of_b_cycles <= 2);
interface.a <= stimuli_for_a;
repeat (number_of_b_cycles) begin
randomize(stimuli_for_b)
interface.b <= stimuli_for_b;
if (stimuli_for_b == 1) number_of_b_assertions += 1;
@(posedge interface.clk);
end
if (stimuli_for_a == 1 && number_of_b_assertions == number_of_b_cycles)
&& number_of_b_assertions > 0)
vpiw.pass_if_sva_started_but_not_finished("IMPLICATION_ASSERT",
"The assertion should have started but not finished!");
@(posedge interface.clk);
... // (continued on the next slide)

## Slide 52: Repetition range with zero (contd.)
a |-> b[*0:2] ##1 c
...
// (continued from previous slide)
interface.c <= stimuli_for_c;
@(posedge interface.clk);
if (stimuli_for_a == 1)
if (number_of_b_assertions != number_of_b_cycles ||
number_of_b_assertions == 0 ||
stimuli_for_c == 0)
vpiw.fail_if_sva_succeeded("REPETITION_RANGE0_ASSERT",
"The assertion should have failed!");
else
vpiw.fail_if_sva_not_succeeded("REPETITION_RANGE0_ASSERT",
"The assertion should have succeeded!");
end // end of test repeat loop

## Slide 53: Sequence disjunction
a |=> (b ##1 c) or (d ##1 e)
repeat (test_loop_count) begin
randomize(stimuli_for_a, stimuli_for_b, stimuli_for_c, stimuli_for_d, stimuli_for_e);
interface.a <= stimuli_for_a;
@(posedge interface.clk);
fork
begin
end
begin
end
join
end
Stimuli for branch: (b ##1 c)
SVA state check based on branch stimuli
Stimuli for branch: (c ##1 d)
SVA state check based on branch stimuli

## Slide 54: Sequence disjunction (contd.)
a |=> (b ##1 c) or (d ##1 e)
...
// Stimuli for branch (b ##1 c)
fork
begin
interface.b <= stimuli_for_b;
@(posedge interface.clk);
interface.c <= stimuli_for_c;
@(posedge interface.clk);
@(posedge interface.clk);
// SVA state check based on branch stimuli
sva_check_phase(interface.a, interface.b, interface.c);
end
join

## Slide 55: Sequence disjunction (contd.)
a |=> (b ##1 c) or (d ##1 e)
...
// Stimuli for branch (d ##1 e)
fork
begin
interface.b <= stimuli_for_d;
@(posedge interface.clk);
interface.c <= stimuli_for_e;
@(posedge interface.clk);
@(posedge interface.clk);
// SVA state check based on branch stimuli
sva_check_phase(interface.a, interface.d, interface.e);
end
join

## Slide 56: Sequence disjunction (contd.)
a |=> (b ##1 c) or (d ##1 e)
// SVA state checking task used in each fork branch
task sva_check_phase(bit stimuli_a, bit stimuli_b, bit stimuli_c);
if (stimuli_a)
if (stimuli_b && stimuli_c)
vpiw.pass_if_sva_succeeded("DISJUNCTION_ASSERT",
"The assertion should have succeeded");
else
vpiw.fail_if_sva_succeeded("DISJUNCTION_ASSERT",
"The assertion should have failed");
endtask

## Slide 57: Tools integration
Simulator independent!

## Slide 58: Availability
  SVAUnit is an open-source package released by AMIQ Consulting
  We provide:
  SystemVerilog and simulator integration codes
  AMBA-APB assertion package
  Code templates and examples
  HTML documentation for API
https://github.com/amiq-consulting/svaunit

## Slide 59: Conclusions
  SVAUnit decouples the checking logic from SVA definition code
  Safety net for eventual code refactoring
  Can also be used as self-checking documentation on how SVAs work
  Quick learning curve
  Easy-to-use and flexible API
  Speed up verification closure
  Boost verification quality

## Slide 60: Q & A
?

## Slide 61: Thank you!